## Slide 1
FAULTS
Segment Outcomes
  Students will be introduced to fault types and causes
  Students will be introduced fault logic reduction and logic minimization.

## Slide 2
Faults
Fault
  A representation of a defect
  Used in computer programs for analyzing defects in electronic components
Defect
  A flaw in the actual hardware

## Slide 3
Fault
Error
  Caused by a defect
  Happens when a defect in hardware causes a line or a gate output to have a wrong value.
Failure
  occurs when a defect causes a misbehavior in the functionality of a system that cannot be reversed or recovered.

## Slide 4
Fault Abstraction
Effects of defects in a circuit may be seen at different levels of abstraction
  i.e., Physical defect of a short between an nMOS transistor gate and its source may be seen at the switch, gate, RT, or system-level

## Slide 5
Gate Fault
Mask misalignment in layout may cause a short between gate of a transistor and its source
  defect translates to T2 switch transistor always staying open.

## Slide 6
Gate Fault
Same defect translates to switch level fault of switch output being open when it is supposed to be 0.

## Slide 7
Functional Faults
Fault that affects functionality of a system
Example:
  Faulty inverter in a multiplexer circuit causes the overall functionality of the multiplexer to be faulty

## Slide 8
Functional Faults
Functional fault of a component at a certain level of abstraction ignores lower-level details of the component
  Only considers the input–output behavior of the component

## Slide 9
Structural Faults
Complexity of analysis for extracting a faulty model for a component can be simplified by analyzing its sub-components.
  (e.g., inverter, AND, and OR gates) and their interconnections (e.g., line i in Fig. 3.5)

## Slide 10
Structural Faults
Consider only interconnection faults
  lump faults on the two ends of an interconnection and of interconnect itself into faults belonging only to the interconnection.

## Slide 11
Structural Faults
Assume that components forming a hardware module are fault free.
Assume only the interconnection of the components may be faulty

## Slide 12
Structural Fault
I.E Inverter fault becomes fault on line i

## Slide 13
Recognizing Faults
Label possible points of failure
Write w as a function of a,b,s
  W_good = (a and (not s)) or (b and s)

## Slide 14
Recognizing Faults
Now assume a failure at I4, stuck at 1
  W_fault = a or (b and s)
Since W_good != W_fault
  I4 can be recognized

## Slide 15
Boolean Difference : Karnaugh maps
Create two k-maps
  One the good function
  the other the faulty function
Input combination where the k-map entries are different represent valid test vectors.
  i.e recognize the faulty circuit from the good one

## Slide 16
Example
stuck-open fault on L3
  l3 and l2 are branches of a fanout whose stem is l1
  l3 stuck open causes the G3 gate to retain its charge forever
  G3 acts like an inverter

## Slide 17
Stuck-at-x faults
Stuck-open
Stuck-at-0
  models' defects on a line or its interconnecting gates such that the line value appears as though it is always 0
Stuck-at-1
  models' defects on a line or its interconnecting gates such that the line value appears as though it is always 1

## Slide 18
Bridging Faults
Defects on neighboring gates and lines may cause a bridging effect on two lines.
  AND bridging
    two bridged lines appear as if they are forming an AND functions which feeds all destinations of the bridged lines
  OR bridging
    Depending on the logic behind and after a bridging fault, the fault may be modeled by an OR function instead of an AND function.

## Slide 19
AND-bridging Faults
Fault between I7 and I3.
.
Tests that detect this faults???

## Slide 20
OR-bridging Faults
Fault between I4 and I7.
.
Tests that detect this faults???