## Slide 1: EEGR 471
Section 1: Simulation

## Slide 2: Section Outline
Introduction
Logic Specifications
Test plans
Simulation
  Cycle vs Event based
Testbenches
  Directed vs Layered
Methodology
Formal

## Slide 3: Section Outcome
Introduce concepts and tools necessary for proper verification
Layout process of performing effective functional verification
Present techniques for applying effective stimulus and monitors design responses as a result.
Explain benefits of bus functional models and how to implement them.

## Slide 4: Prior Knowledge
This section is focused on verification of described/simulatable hardware design…. So VHDL or Verilog
  Students are expected to have basic knowledge of one of these description languages.
We will be reviewing and verifying digital designs, so basic knowledge of logic design.
We will be going over SystemVerilog which in simulation is mostly class based.
  So… some understanding of Object-Oriented Programming is expected.

## Slide 5: BACKGROUND
ICs are an integral part of daily life in 2023.
Included in everything:
  Phones
  TV’s
  Laptops
  Watches
  Earphones
  and yes, even Fridges.

## Slide 6: HW/SW Systems
Complexity in Lines of Code
Notes: Adapted from : https://ati.ttu.ee/~jaan/verification/1_introduction%20english.ppt

## Slide 7: Building blocks: Logic Gates
At the heart of IC’s are logic gates.. Combined into complex systems

## Slide 8: Sea of Gates

## Slide 9: Logic Design: Early Days
Write out logic by hand
  Truth Tables, K-maps, State tables.

## Slide 10: Logic Design: Middle Ages
Schematic Entry
  Draw design gate by gate.
  then map to available resources.
Notes: Cs.cornell.edu/courses/cs3410/2019sp/riscv/interpreter/

## Slide 11: Logic Design: HDL and Synthesis
When are a thousand words worth more than a picture?
HDL: describe the logic, let the synthesis tool turn it into gates

## Slide 12: Design automation
productivity gap
  58% versus 21% annually
transistors
on the die
Tehnology’s
capabilities
Designer’s productivity
today
time
40
60
70
30
40
2
30
2
3
2
System
design
Logic
design
Physical
design
Simulation
Schematic
entry
Placement &
routing
Hierarchy,
generators
Logic synthesis
High-level synthesis /
System-level synthesis
Specialized
high-level synthesis
< 1979
~ 1983
1986
1988-92
1992-95
~1996-...
Person months /
20 000 logic gates
10
2
30
50
2
Notes: Adapted from: https://ati.ttu.ee/~jaan/verification/1_introduction%20english.ppt

## Slide 13: Digital IC FLOW
Requirements Negotiation | Verification
Specification | Verification
RTL Logic Design | Verification
Synthesis | Verification
Implementation & (Place & Route) | Verification
Bitstream or Layout (GDSII) | Validation | Emulation
Specification
Requirements Negotiation
RTL Logic Design
Synthesis
Bitstream or Layout (GDSII)
Specification Review
Test Plan
RTL Simulation
Formal Verification
Post- Synthesis Verification
Equivalence checking
Validation
Emulation
Implementation & (Place & Route)
Post-implementation Verification

## Slide 14: Verification Engineers
Some figures:
2-4 verification engineers per designer
Verification takes 70-85 % of total cost of chip design
Why Verification matters?
Notes: Adapted from https://ati.ttu.ee/~jaan/verification/1_introduction%20english.ppt

## Slide 15: Verification Engineers
*https://www.ziprecruiter.com/Salaries/Entry-Level-Design-Verification-Engineer-Salary
Notes: Adapted from https://ati.ttu.ee/~jaan/verification/1_introduction%20english.ppt

## Slide 16: Why Verification Matters
$250+ million investment just to get started.
Bugs found pre-fab cost project lines of Code; bugs found after tapeout cost millions.. Possible harm to people
Re-spin (design correction and re-fabrication) is long and costly
  Around $25 million per re-spin.
Best chance of minimizing bugs ???
  Proper Verification

## Slide 17: When things go wrong...
1985-1987 - Therac-25 medical accelerator. At least 5 patients die.
1993 - Intel Pentium floating point divide. Costs te company $475 million.
June 4, 1996 - Ariane 5 Flight 501. Rocket disintegrates 40 seconds after launch.
February 2010 - Toyota Prius failure. Toyota loses its market share.
Notes: Adapted from: https://ati.ttu.ee/~jaan/verification/1_introduction%20english.ppt

## Slide 18: The first bug found
Harvard Mark II system, 1945
Notes: Adapted from: https://ati.ttu.ee/~jaan/verification/1_introduction%20english.ppt

## Slide 19: Types of verification
Mixed-signal
Digital
Analog, RF, etc.
Functional, timing, layout, electrical
Notes: Adapted from: https://ati.ttu.ee/~jaan/verification/1_introduction%20english.ppt

## Slide 20: Digital Logic verification
Functional
Formal
Post-Synthesis
NOTE: In this class, we are going to tie everything to a specification
Notes: Adapted from: https://ati.ttu.ee/~jaan/verification/1_introduction%20english.ppt

## Slide 21: Functional Verification
Process of demonstrating that a design works as specified.
  I.E design functions as it is expected to by whoever asked for it to be created.

## Slide 22: Formal Verification
Process of converting the behavior described in the specification requirements into mathematical functions known as formal model.
Then checking that the design satisfies properties also derived from the specification.

## Slide 23: Post-Synthesis Verification
Process of demonstrating that the design, once converted from HDL into low level gates and implemented in the physical world still behaves as described in the specification.

## Slide 24: Verification flow

## Slide 26: Lab 1
Get ubuntu VM running/ School server instance??
Installs
  vs code
    TerosHDL extension
  verilator
  Iverilog
  Yosys
  pyverilog

## Slide 27: Requirement and Plans
Segment Outcomes
  Students will be introduced to functional hardware requirements.
  Students will be introduced to logic test plans.
  Students will learn how to derive test plans from hardware specifications.

## Slide 28: Functional Logic Specification
Functional requirements of how what a design is expected to do at completion…. Not how but WHAT.
Should be at the bounded by the abstraction level of design.
  I.E. CPU spec should be at memory/bus/instruction level. ALU requirements should be in a separate ALU spec

## Slide 29: Functional Logic Specification
Requirements should be limited to input and output ports
Unnecessary requirements lead to confusion and should be pushed back against

## Slide 30: Example: UART Tx/Rx
UART: Universal Asynchronous Receiver/Transmitter.
2 wire serial bus
  TX and RX
Baudrate: clock to baud clock.
  i.e 50MHZ clk to 115200 baud = 50000000 / 115200 or…
  434.027778 clocks per serial baud tick.
  Round down???

## Slide 31: Example: UART Tx/Rx CTND.
UART frame consists of 5 elements:
  Idle (logic high)
  Start bit (logic low (0))
  Data bits
  Parity bit
  Stop (logic high (1))

## Slide 32: Uart Design Spec: Ports
Inputs:
  clk_50m: 50Mhz clock
  wr_en: write enable
  rx: uartreceive signal
  rdy_clr: clear ready signal
  din: 8 bit data into tx side
Outputs:
  tx: uart transmit signal
  tx_busy: transmit busy signal
  rdy: uart rx ready/ valid rx signal
  dout: 8 bit rx data

## Slide 33: Uart Design Spec: RX Functional Requirements
Module shall: track transactions on it rx signal following the uart protocol.
Module shall: output received data on dout immediately following a uart rx transaction.
Module shall: output received data on dout immediately following a uart rx transaction.
Module shall: deassert rdy one clock cycle after rdy_clr is asserted.

## Slide 34: Uart Design Spec: TX Functional Requirements
Module shall: transmit transactions on it tx signal following the uart protocol.
Module shall: when wr_en is asserted, transmit the data in din on the tx line as a uart tx transaction.
Module shall: only while actively transmitting, assert the tx_busy signal, otherwise deassert tx_busy.

## Slide 35: Uart Design Spec: TX Functional Requirements
Requirements Negotiation:
  Module shall: only while actively transmitting, assert the tx_busy signal, otherwise deassert tx_busy.
  Module shall: while actively transmitting, assert the tx_busy signal.
  Module shall: while not actively transmitting, deassert tx_busy.

## Slide 36: Universal Serial Bus (USB)
a two-wire serial communication link that runs at either 1.5 or 12 megabits per second (mbs).
Vdd, D+, D-, GND
USB has many layers. We’ll focus on Protocol layer

## Slide 37: USB Bus Topology
Host
Hub
Hub
Hub
Hub
Func
Func
Func
Hub
Func
Func
USB connects USB devices with the USB host
Hub can be connected to host/hub/func
Func is the device being connected to host

## Slide 38: Uart Protocol Layer
Transmitted in packets (LSB to MSB)
  Sync field
  PID
  Address
  Data
  Endpoint
  CRC
  EOP

## Slide 39: Test Plan
Specification document that captures all the details needed for verifying a given design.
  Will encompass all aspects of the design from concept to delivery.
Verification engineer is responsible for developing this plan initially as he understands the details of the DUT (Design under Test).
Verification plan is a subsegment of the overall Testplan.

## Slide 40: Test Plan
Critical in avoiding failures later in a project.
  which can include bug escapes
  re-working several infrastructure work / time crunches
  loosing on quality/features.
What, How, When.

## Slide 41: What To Test
Test plan should list down details on what all features of design to be verified.
List all features that should will be tested as individual test items.
Account for all supported design configurations (register settings) under which features should be tested as test plan items.

## Slide 42: What to Test ctd.
capture specific micro-architectural cases that needs to be ensured for correctness.
  state machines, FIFOs, arbitration and other logical block interactions
specific stimulus patterns, interactions, high level usage scenarios, potential deadlock/livelock conditions

## Slide 43: How to Test
Determine the best way to verify each test item.
Most items will be checked by functional verification and constrained random stimulus.

## Slide 44: How to Test
Some requirements will be best covered by Formal Verification
Some can be checked by emulation
Some items will be checked by Visual inspection
Figure out how best each of the items can be verified

## Slide 45: When to Test
Project timeline.
  Verifiers are expected to test more and more, in less and less time.
Test plan needs to capture estimates for timeline of completion.
Estimates should be modular. Parallelize when possible.
Determine Item priorities based on schedule.
  Usually at least three:
  High, Medium, Low

## Slide 46: Problems during Testing
Errors in spec, implementation, language
No way to detect bugs in the spec, because reference object is missing.
  Thus: verification by redundancy.
Problem: How to measure verification quality i.e. coverage? (except in equivalence checking)

## Slide 47: Test Plan Contents
Verification Plan
  Pre-synthesis
Validation Plan
  Post-Synthesis
HASS and Halt Plan
  Stress testing
Acceptance Criteria
  EMF, Board Testing, Electrical paths… ETC.

## Slide 48: Verification Plan
Closely tied to the hardware specification and contains a description of what features need to be exercised and the techniques to be used.
Steps may include:
  Directed or random testing
  Assertions
  HW/ SW co-verification
  Emulation
  Formal proofs
  Use of verification IP.
SystemVerilog for Verification

## Slide 49: Verification Basics
The most important principle you can learn as a verification engineer is: “Bugs are good.” Don’t shy away from finding the next bug, do not hesitate to ring a bell each time you uncover one, and furthermore, always keep track of each bug found. – some guy probably
SystemVerilog for Verification

## Slide 50: Revisit Uart Ports
Inputs:
  clk_50m: 50Mhz clock
  wr_en: write enable
  rx: uartreceive signal
  rdy_clr: clear ready signal
  din: 8 bit data into tx side
Outputs:
  tx: uart transmit signal
  tx_busy: transmit busy signal
  rdy: uart rx ready/ valid rx signal
  dout: 8 bit rx data

## Slide 51: Revisit Uart RX Functional Requirements
Module shall track transactions on it rx signal following the uart protocol.
Module shall output received data on dout immediately following a uart rx transaction.
Module shall output received data on dout immediately following a uart rx transaction.
Module shall deassert rdy one clock cycle after rdy_clr is asserted.

## Slide 52: Revisit Uart TX Functional Requirements
Module shall transmit transactions on it tx signal following the uart protocol.
Module shall, when wr_en is asserted, transmit the data in din on the tx line as a uart tx transaction.
Module shall, only while actively transmitting, assert the tx_busy signal, otherwise deassert tx_busy.

## Slide 53: Verification plan: How do we verify this
RX side
  We’ll need to drive RX
  Verify that dout outputs correct data
  Verify that rdy is 1 after transfer.
  Verify that rdy goes low when rdy_clr is 1
TX side
  We’ll need to put data on din then assert wr_en
  Verify that it transmits the data on din.
  Verify that tx_busy is on when transmitting.
  Verify that it’s transmitting at the right frequency

## Slide 54: Verification plan: How do we verify this
What about clk
  Recall baud clock is 50000000 / 115200 = 434.027
  Going to have some offsets
  What is the error margin on the design?
  Can it handle a “bad” clock.

## Slide 55: Logic Simulation Segment
Outcomes
  Students will be introduced to logic simulation concepts
  Students will understand the basic algorithms behind HDL simulators.
  Students will understand the difference between cycle based and event based logic simulators.

## Slide 56: Simulation-based verification

## Slide 57: Logic Simulation
Need a way to check that RTL (Register transfer level) Hardware description is doing what we expect it to do.
Simulate how logic designed will behave when given certain stimulus.
Simulation environment is usually controlled by a top level testbench that instantiates the design as a DUT.
Often with a waveform to view data flow into and through design.
Cycle-Based and Event-Based

## Slide 58: Circuit Modeling
Electronic system level
  SW + HW
  Cycle accurate modeling
  C/C++, SystemVerilog, Python
Register-Transfer Level (RTL)
  Define bit and timing accurate architecture
  VHDL and Verilog. Python? C/C++?
Logic/cell/ gate
  Interconnected Boolean operation gates
  Work well for logic design, verification, testing.

## Slide 59: Level of Circuit Modeling
Switch
  Interconnets of “Perfect” transistor switch
  Most simulation is at this level
Timing
  Use transistors with device models.
    i.e switch on/off time
  Post Place & Route verification
Circuit
  Lowest level, truest accuracy available in simulation
  Get timing by solving interdependent equations of branch/loop current and node voltage

## Slide 60: Logic State for Simulation
Two state (0,1) for combinational and sequential circuits that are properly initialized.
  Note: this is the behavior in hardware… no “x” in HW.
Four states (0,1,X,Z) for uninitialized sequential circuits.
  Z for high impedance, used when you aren't driving the output of a signal, so that some other process can drive it.
  X(Unknown State) for cases when logic value cannot be calculated.
    Such as, uninitialized FF, memory, bus, etc.

## Slide 61: Logic propagation of X
AND | 0 | 1 | X
0 | 0 | 0 | 0
1 | 0 | 1 | x
X | 0 | X | X
OR | 0 | 1 | X
0 | 0 | 1 | X
1 | 1 | 1 | 1
X | X | 1 | X
What happens when we treat “x” as a signal
  Not x = x
  x+x =x
Problem?
  We start to lose information
  Output should be 1 but due to x’s we get x.

## Slide 62: High Impedance
Floating state: node with no path to vdd or gnd.
Logic state of Z can be determined dynamically
  Single floating node
    Keeps value driven before becoming floating
  A set of floating node get connected
  A floating node connected to Vdd/Gnd becomes 1/0.
  Multiple sources driving a floating node, the value depends on strength of the driving logic.

## Slide 63: Modeling Levels and Signals
Level | Circuit Description | Signal | Timing Resolution | Application
ESL | SystemC | 0,1 | Transaction | System
Behavior | HDL | 0,1 | Cycle | Architecture
Logic | Gate-level HDL | 0,1,X,Z | Zero, unit, multiple cell delays | Logic design and test
Switch | Transistor, RC interconnects | 0,1,X | Zero, possible gross-grain timing | Full-custom logic verification
Timing | SPICE | Analog | Fine-grain time | Timing verification
Circuit | SPICE | Analog | Continous time | Timing/analog verification

## Slide 64: Simulators
Open Source
  Verilator – C/C++
  Icarus Verilog - Verilog
  GHDL – VHDL
Commercial
  QuestaSim
  Xcellium

## Slide 65: Simulation Phases
Coordinate the testbench so all the code for a project works together.
Build
  Generate Configuration
  Build Environment
  Reset the DUT
  Configure the DUT based on generated configuration
Run
  Start environment
  Run the test
Wrap-up
  wait for the final transactions to drain out of the DUT
  Report.
SystemVerilog for Verification

## Slide 66: Simulation: Cycle based
Computes steady state response of a circuit at each clock cycle.
It does not simulate detailed circuit timing, but instead computes the steady state response of a circuit at each clock cycle.
User observes circuit signals once per clock cycle. Cycle based simulators work only with synchronous designs.

## Slide 67: Simulation: Cycle based
Available simulators that are cycle based include:
  Verilator
  VCS
  NCSIM

## Slide 68: Simulation: Cycle based
Lack of detailed circuit timing means the user cannot see the glitch behavior of signals between clock cycles.
Notes: https://i0.wp.com/semiengineering.com/wp-content/uploads/2019/07/Synopsys_which-glitch-is-which-fig1.png?ssl=1

## Slide 69: Cycle-based
Circuit is simulated by executing compiled code of the circuit.
Levelization
  To ensure that a signal is evaluated after all its sources are evaluated
Levelization Process
  Assign all Primary Inputs to 0
  Level of gate G is Lg = 1 + max(L1,L2,..)
    Where Li’s are G’s input gates
Level 0: a, b, c, d
Level 1: e, f
Level 2: g, h

## Slide 70: Levelization algorithm flow

## Slide 71: Example of Levelization
Order produced by flow
  G1 => G2 => G3 => G4
  G1 => G3 => G2 => G4

## Slide 72: Cycle-based simulation
Effective for 2-state (0,1) simulation
  Very fast
  Can be compiled directly into machine language
Mostly useful for functional verification, when timing is not analyzed
  Will miss glitches.. i.e signals changing in between clock edges.

## Slide 73: Verilator
  Verilator is a tool that compiles Verilog and SystemVerilog sources to highly optimized (and optionally multithreaded) cycle-accurate C++ or SystemC code.
  The converted modules can be instantiated and used in a C++ or a SystemC testbench, for verification and/or modelling purposes.

## Slide 74: Verilator HDL to C Conversion
The top wrapper looks like the top Verilog module.
Inputs and outputs map directly to bool, uint32_t, uint64_t, or array of uint32_t’s:
Notes: Verilator Internals, July 2005

## Slide 75: Downsides of Cycle-based simulation
Zero-delay model
  Perfect switch assumption
  Timing problems. i.e glitches, race conditions are ignored
Simulation time
  Every circuit is evaluated at every cycle even though typically only 1-10% of signals change at any time.

## Slide 76: Event-Based simulation
Event is defined as a change in value of a signal, input or internal.
Event based simulator evaluates a gate (element) only if one or move events occur at its inputs
  Minimizes the amount of computation done
  Follows path of signal flow

## Slide 77: Simulation: Event Based
Intermediary and output signals update whenever there’s a change in an input signal.
Allows for simulating designs with possible glitches.

## Slide 78: Event-Based simulation
Allows for post-synthesis and timing-based simulation.
Event based simulation very slowed compared to Cycle based since it must simulate much more behavior.

## Slide 79: Event-Based simulation
Available Simulators that are Event Based:
  Most commercial simulators are event based
  QuestaSim
  Vivado
  Xcelium
  Icarus Verilog. *Open source*

## Slide 80: Basic Principles
Designed to eliminate unnecessary gate simulations without introducing an unacceptable amount of additional testing.
An event is defined to be a change in the value of a net.

## Slide 81: Basic Principles: Event Based
Main function of an Event Driven simulator is to detect events, and schedule gate simulations in response to them
Two times when it is necessary to test nets for changes
    when a new input vector is read
    immediately after a gate is simulated.

## Slide 82: Event-Based Sim Basic Principles Ctd.
Two times when it is necessary to test nets for changes
    when a new input vector is read
    immediately after a gate is simulated.

## Slide 83: Input Simulation
When an event is detected, an event structure must be created and stored for future processing.
Event Queue will be used to store any events that have been detected and not yet processed.
Notes: Algorithm 3-1. Input Vector Processing.

## Slide 84: Input Processing Algo.

## Slide 85: Input Vector Processing
Consider simulating with two consecutive input vectors
  (1,1,0,0,1,0)
  (0,0,0,0,1,1)
Vectors differ in three positions
Events must be created for Net A,B,F.

## Slide 86: Event Processing
First part of event processing is to copy net values from the event structures into permanent storage.
second part is to schedule all gates in the fanout of a net for simulation.
  place the identification of the gate into another queue called the Gate Queue.

## Slide 87: Event Processing Algo.

## Slide 88: Gate Processing
After Event Processing, simulate each gate in gate queue
Also, necessary to test the output of each simulated gate for changes and schedule events.

## Slide 89: Gate Processing
Gate simulation creates new events and places them in the Event Queue.
Simulation of an input vector consists of a single call to the Input Processing Routine, and several calls to the gate and event processors.

## Slide 90: Gate Processing Algo.

## Slide 91: Simulate Vector Alg.

## Slide 92: Timing Model
Event based simulation provides a unit-delay model (timescale).
  Unlike Cycle-Based simulation which provides zero-delay model (perfect switch).
Example
  Initial Values: A=0, B=0, Next Values: A=1, B=1
  Cycle-Based Simulation will leave Q at Zero
  What happens in Event-Based??

## Slide 93: Event-Based Timing Simulation
  Input 0 of G2 will propagate first, Q = 1
  Input 1 of G2 will then become 0, Q = 0;

## Slide 94: Big Picture: Cycle based vs Event Based

## Slide 95: Lab 2
Use pyverilog to parse simple Verilog file
Create two simulators that can accept test vectors in csv format.
  Cycle-based
  Event-based
Should output a vector or value changes.

## Slide 96: Frameworks Segment
Students will be introduced to Non-synthesizable SystemVerilog and its benefits.
Students will be introduced to cocotb and how it compares to SystemVerilog.

## Slide 97: Non-synthesizable SystemVerilog
The vision of SystemVerilog was to first expand on the abstract capabilities of synthesizable code.
significantly add all the features known to be necessary for verification.
A strict superset of the previous Verilog standards.
SystemVerilog for Verification

## Slide 98: Non-synthesizable SystemVerilog
The benefits of having a single language and a single coherent run-time environment cannot be expressed enough.
Including the design, testbench, and assertion constructs in a single language is that the testbench has easy access to all parts of the environment without requiring specialized APIs.
SystemVerilog for Verification

## Slide 99: Data Types
Logic
  4 state single bit type
Fixed-Size Arrays
  i.e: my_array[5]
Queue
  i.e: my_queue[$]
  Provides sorting, size.
Typedef
  Create new types
SystemVerilog for Verification

## Slide 100: Structs
Structs
  allows you more control in how data is laid out in memory by using packed structures.
  A packed structure is stored as a contiguous set of bits with no unused space.
  i.e:
    typedef struct packed logic[7:0] {r,g,b) pixel_t;
SystemVerilog for Verification

## Slide 101: Enums
Enums
  strong variable type that is limited to a set of specified names
  instruction opcodes or state machine values.
    i.e:
      typedef enum {ERROR=0, FIRST=1, Second = 2} my_enum_e;
SystemVerilog for Verification

## Slide 102: Data Types
Linked Lists
  Yes, they exist in SystemVerilog.
  NO, do not use them.
SystemVerilog for Verification

## Slide 103: Tasks, Functions, and Void Functions
task can consume time while a function cannot.
A function cannot have a delay
  #100, a blocking statement such as @(posedge clock) or wait(ready), or call a task
SystemVerilog for Verification

## Slide 104: Tasks, Functions, and Void Functions
Why functions????
  Can be synthesized “sometimes”
  Can call at the beginning/ or very end of a test.
Void Functions… don’t have a return type.
SystemVerilog for Verification

## Slide 105: Time-unit
use timeunit and timeprecision or ‘timescale to unambiguously specify a time value plus units
  i.e : 0.1ns or 20ps.
  timeunit 1ns; then #1 = wait 1 nano second
SystemVerilog for Verification

## Slide 106: Object Oriented Programming
Goal of a testbench is to apply stimulus to a design and then check the result to see if it is correct.
data that flows in and out of design is grouped together into transactions.
easiest way to organize the testbench is around the transactions, and the operations that you perform.
In OOP, the transaction is the object that is focus of your testbench.
SystemVerilog for Verification

## Slide 107: Class
Basic building block containing routines and variables.
In Verilog, you need to instantiate a module to use it.
Encapsulates data together with the routines that manipulate it.
Handle
  a pointer to an object.
  An OOP handle is like the address of the object
  stored in a pointer that can only refer to one type.
SystemVerilog for Verification

## Slide 108: Create Object
SystemVerilog for Verification

## Slide 109: Inheritance
Main “power” of OOP
  take an existing class, i.e such as a transaction
  selectively change parts of its behavior by replacing routines
  but without having to change the surrounding infrastructure.
SystemVerilog for Verification

## Slide 110: Interface
Encapsulate related Signals into a block
Same interface can be re-used in other projects
Easier to connect DUT to other verification components I.E classes.
Note:
  Interface is essentially a module.. Anything you can do in a module you can do in an interface……
    Except it can’t be top module.
Classes must instantiate “Virtual” Interfaces.

## Slide 111: Uart Interface

## Slide 112: Virtual Interface
A virtual interface is a variable that represents an interface instance.
Why Virtual Interface
  SystemVerilog interface is static in nature, whereas classes are dynamic in nature.
    Remember an interface IS a module
  Not allowed to declare the interface within classes but can refer to or point to the interface.
Virtual interface is a variable of an interface type
  used in classes to provide access to the interface signals.

## Slide 113: Uart Class

## Slide 114: Callbacks
“hook” to inject new code without modifying the original classes.
Your driver may want to:
  Inject errors, Drop the transaction, Delay the transaction, Synchronize transaction with others, Put the transaction in the scoreboard, Gather functional coverage data.
SystemVerilog for Verification

## Slide 115: Driver Callbacks
SystemVerilog for Verification

## Slide 116: cocotb
Open source coroutine-based cosimulation testbench environment for verifying VHDL and SystemVerilog RTL using Python.
cocotb is all about verification productivity.
It allows developers to focus on the verification task itself, and stop fighting with language limitations.
Cocotb.org

## Slide 117: Cocotb: Creating a Test
typical cocotb testbench requires no additional HDL code.
The DUT is instantiated as the toplevel in the simulator without any HDL wrapper code.
access all internals of your design, i.e signals, ports, parameters, etc. through an object that is passed to each test, usually called dut.
Things to note:
  Use the @cocotb.test() decorator to mark the test function to be run.
  Use .value = value to assign a value to a signal.
  Use .value to get a signal’s current value.
Cocotb.org

## Slide 118: Cocotb: simple testbench
drive 10 periods of a square wave clock onto a port clk of the toplevel.
After,
  the clock stops
  the value of my_signal_1 is printed
  value of index 0 of my_signal_2 is checked to be 0.
Cocotb.org

## Slide 119: Cocotb: Makefile
In order to run a test, you need to create a Makefile that contains info about your project.
SIM
  default simulator
TOPLEVEL_LANG
  language of your top module
TOPLEVEL
  Name of Top module
MODULE
  basename of python test file
Cocotb.org

## Slide 120: Testbench Segment
Outcomes
  Students will learn the basic concepts of a testbench
  Students will learn how and utilize directed testbenches.

## Slide 121: Testbench
An overall environment that instantiates or contains the design under test (DUT) with the abilities to apply inputs the design and monitor outputs.

## Slide 122: Basic Testbench Functionality
The purpose of a testbench is to determine the correctness of the design under test (DUT).
This is accomplished by the following steps.
  Generate stimulus
  Apply stimulus to the DUT
  Capture the response
  Check for correctness
  Measure progress against the overall verification goals

## Slide 123: Testbench Basics
Template
  Dummy template that declares inputs to and outputs from Design under test (DUT).
  Then instantiates the DUT.

## Slide 124: Testbench Components
If the real device connects to AMBA, USB, PCI, and SPI buses
  must build equivalent components in your testbench that can generate stimulus and check the response.
high-level transactors that obey the protocol, but execute more quickly
SystemVerilog for Verification

## Slide 125: Testbench components
SystemVerilog for Verification

## Slide 126: Directed Testing
Manually write stimulus vectors that exercise features in the DUT.
Simulate the DUT with these vectors
Manually review the resulting log files and waveforms to make sure the design does what you expect.
Once the test works correctly, you check off the test in the verification plan and move to the next
SystemVerilog for Verification

## Slide 127: Directed Testing Pros?
Incremental approach makes steady progress
produces almost immediate results
  since little infrastructure is needed when you are guiding the creation of every stimulus vector.
Given enough time and staffing, directed testing is sufficient to verify many designs.
“I bought five watches the other day. I have a lot of time on my hands….”
SystemVerilog for Verification

## Slide 128: Directed TB: Uart
Check that data in == data out.
Clear ready
Flag if fails
Flag if fails

## Slide 129: Directed Testing Cons?
What if you do not have the time or resources to carry out the directed testing approach?
Might always make forward progress but… the slope remains the same.
Test-time scales with design complexity
  When design becomes more complex, will take twice as long to verify
  Or twice as many people verifying… Project managers will love that .
SystemVerilog for Verification

## Slide 130: Directed test progress
SystemVerilog for Verification

## Slide 131: What then?
You need a methodology that finds bugs faster in order to reach the goal of 100% coverage.
You need Methodology
SystemVerilog for Verification

## Slide 132: Methodology Segment
Student will learn the basic concepts of design verification methodology.
Sub-Segments
  Layered Testbenches
  Simulation Phases
  Constrained Random Stimulus
SystemVerilog for Verification

## Slide 133: Methodology Basics
Layered testbench using transactors
Constrained-random stimulus
Bus Functional Models (BFM)
Common testbench for all tests
Test-specific code kept separate from testbench
Functional coverage
SystemVerilog for Verification

## Slide 134: Layered Testbench
key concept for modern verification is the layered testbench.
may seem to make the testbench more complex… but it helps to make your task easier
  dividing the code into smaller pieces that can be developed separately.
SystemVerilog for Verification

## Slide 135: Layered Testbench
Don’t try to write a single routine that can randomly generate all types of stimulus
  both legal and illegal
  Inject errors with a multi-layer protocol.
routine quickly becomes complex and unmaintainable
SystemVerilog for Verification

## Slide 136: Flat v.s Layered
SystemVerilog for Verification

## Slide 137: Methodology: BFM
To the DUT they look like real components … but are part of the testbench, not RTL.
Write “rtl-like” functionality in software without worrying about latches/timing/combinational delays, glitches.
SystemVerilog for Verification

## Slide 138: Methodology: Building blocks
What goes into a methodology testbench block?
Layers
  Signal Layer
  Functional Layer
  Scenario Layer
  Test Layer
SystemVerilog for Verification

## Slide 139: Signal and command layers
SystemVerilog for Verification

## Slide 140: Signal and command layers
Signal layer that contains the design under test and the signals that connect it to the testbench
Driver: drives DUT’s inputs with single commands such as bus read or write.
Monitor: driven by the DUT’s output, takes signal transitions and groups them together into commands.
SystemVerilog for Verification

## Slide 141: Methodology: Driver
Driver
  Drives the generated stimulus to the design.
  Could be as simple as a wire….
  Or as complex as modeling instructions from rom to processor

## Slide 142: Driver: UART

## Slide 143: Methodology: Monitor
Monitor
  Monitor the design input-output ports to capture design activity
  Track data going into and out of the DUT.
  Could also use to confirm driver is behaving correctly

## Slide 144: Monitor: UART

## Slide 145: The functional layer
Functional layer feeds the command layer
Agent: receives higher-level functions and breaks them into individual commands for the driver.
Checker: compares commands from monitor with those in the scoreboard.
Scoreboard: receives commands from agent and predicts the results of the transaction.
SystemVerilog for Verification

## Slide 146: The functional layer
SystemVerilog for Verification

## Slide 147: Methodology: Testbench Components
Scoreboard
  Checks output from the design with expected behavior
  Takes in data from both input and output of the design
  Confirms that data out was what was expected by the model.

## Slide 148: Scoreboard UART RX

## Slide 149: Scenario Layer
Generator in the scenario layer drives the functional layer
Orchestrates all these steps with constrained-random values for parameters such as track size and memory location.
SystemVerilog for Verification

## Slide 150: Methodology: Generate
Generate
  Creates stimulus likely to “stress” design
  Ideally trigger as many parts of the design as possible
Example: MP3 player that can do many thing concurrently
  plays music from storage
  downloads new music from a host
  respond to input from the user
    such as volume and track controls.
Each of these operations is a scenario.

## Slide 151: Generate: Uart

## Slide 152: Test Layer
Test:
  top level of the testbench
  contains the constraints to create the stimulus.
  Think of a conductor who does not play any musical instrument, but instead guides the efforts of others.
SystemVerilog for Verification

## Slide 153: Test: UART

## Slide 154: Parallel random testing
Running with multiple seeds broadens the coverage of your test and leverages your work.
Need to choose unique seed
  Time of day? What if you have multiple servers kicking off jobs that start at the same time?
  Modern simulators have pretty good seed generation
SystemVerilog for Verification

## Slide 155: FORK
Fork???
  Multi-thread/ Concurrent Operation
  Hardware operates Concurrently, so test must too.
Fork-join: finish when all threads finish
fork-join_any: finish when any thread finish
Fork-join_none: finish immediately run threads in the background.
Each is useful in different situation

## Slide 156: Fork Example
All happening at the same time..
  At least from the simulations point of view

## Slide 157: Functional coverage
Functional coverage:
  measures the progress of all tests in fulfilling the requirements in the verification plan.
monitor stimulus going into device, its reaction and response
  determine what functionality has been exercised
changes through the project as the various criteria complete.
  constantly being modified
  not part of the environment
SystemVerilog for Verification

## Slide 158: Functional Coverage Roll Up
Combine data from one or more simulations into a report.
Feedback from functional coverage to stimulus
  change the test to find new approaches to reach uncovered areas of the design
  Example: change the constraint weights based on types of transactions that have been previously generated
SystemVerilog for Verification

## Slide 159: Coverage convergence
SystemVerilog for Verification

## Slide 160: Test progress with and without feedback
SystemVerilog for Verification

## Slide 161: Full Picture
SystemVerilog for Verification

## Slide 162: Constrained-Random Stimulus Segment
Explain the basics and benefits of randomized input to the DUT
SystemVerilog for Verification

## Slide 163: Constrained-Random Stimulus
Simulator generates the stimulus.
  But not totally random values.
Use the verification language to describe the format of the stimulus
  “address is 32-bits, opcode is X, Y, or Z, length < 32 bytes”
  Allow the simulator to pick values that meet the constraints.
SystemVerilog for Verification

## Slide 164: Constrained-Random Stimulus - 2
Coverage may overlap other tests or may explore new areas that you did not anticipate.
If these new areas find a bug, you are in luck! If the new area is not legal, you need to write more constraints to keep away
SystemVerilog for Verification

## Slide 165: What Should You Randomize?
First thing that you might think of is the data fields.
  Easy peazy: just call $random, or c/python alternative
Problem?
  gives a very low payback in terms of bugs found.
  primary types of bugs found with random data are data path errors
    perhaps with bit-level mistakes.
  Need to find bugs in the control logic.
SystemVerilog for Verification

## Slide 166: What Should You Randomize?
Need to think broadly about all design input, such as:
  Device configuration
  Environment configuration
  Input data
  Protocol exceptions
  Delays
  Errors and violations
SystemVerilog for Verification

## Slide 167: Input Data
Think of implementing a transaction such as a bus write and filling the data fields with random values
  Should be easy if you have carefully prepared your transaction classes.
need to anticipate any layered protocols and error injection, plus scoreboarding and functional coverage.
SystemVerilog for Verification

## Slide 168: Randomize: configuration
Should randomize the entire environment configuration
  including the length of the simulation
  number of devices, and how they are configured.
need to create constraints to make sure the configuration is legal.
Consider other environment parameters include test length, error injection rates, delay modes, etc.
SystemVerilog for Verification

## Slide 169: Delays and synchronization
How fast should your testbench send in stimulus?
Use constrained random delays to help catch protocol bugs.
test that uses the shortest delays won’t create all possible stimulus.
subtle bugs are often revealed when intermittent delays are introduced.
SystemVerilog for Verification

## Slide 170: Genenerate Delays

## Slide 171: Delays and Synchronization
When possible, coordinate various drivers so they can communicate at different relative timing.
What if the inputs arrive at the fastest possible rate, but the output is being throttled back to a slower rate?
What if stimulus arrives at multiple inputs concurrently?
What if it is staggered with different delays?

## Slide 172: Protocol exceptions
If something can go wrong in the real hardware, you should try to simulate it.
Look at all the errors that can occur.
What happens if a bus transaction does not complete?
Invalid operation is encountered?
SystemVerilog for Verification

## Slide 173: Protocol Exceptions: Be provocative!
Does the design specification state that two signals are mutually exclusive?
  Drive them both and make sure the device continues to operate.
Be provocative!
SystemVerilog for Verification

## Slide 174: Coverage Segment
Students will learn the different types of coverage and how they roll up into test acceptance and confidence.

## Slide 175: Coverage Type
Coverage is a generic term for measuring progress to complete design verification.
coverage tools gather information during a simulation and then post-process it to produce a coverage report.
SystemVerilog for Verification

## Slide 176: Coverage Type
can use coverage report to look for coverage holes and then modify existing tests or create new ones to fill the holes.
iterative process continues until you are satisfied with the coverage level.
SystemVerilog for Verification

## Slide 177: Code Coverage
Code coverage measures how thoroughly your tests exercised the “implementation” of the design specification, and not the verification plan.
Untested design code could conceal a hardware bug or may be just redundant code.
SystemVerilog for Verification

## Slide 178: Types of code coverage
line coverage : measuring how many lines of code have been executed which
path coverage: paths through the code and expressions have been executed
toggle coverage: which single-bit variables have had the values 0 or 1
FSM coverage: which states and transitions in a state machine have been visited
SystemVerilog for Verification

## Slide 179
Code coverage: block coverage
SystemVerilog for Verification

## Slide 180: 100% Code Coverage???
Job done?? Not exactly
What about actual functionality?

## Slide 181: Functional coverage
Functional coverage is tied to the design intent and is sometimes called “specification coverage,”
what happens if a block of code is missing from the design?
  Code coverage cannot catch this mistake, but functional coverage can.
SystemVerilog for Verification

## Slide 182: Functional coverage
Functional coverage is tied to the design intent and is sometimes called “specification coverage,”
what happens if a block of code is missing from the design?
  Code coverage cannot catch this mistake, but functional coverage can.
SystemVerilog for Verification

## Slide 183
Sequence b,a,b,a,b,a,b,a,... gives 66.67% of state coverage, as S1 and S2 traversed (2 out of 3).
S4 is illegal state, thus max state coverage is 75%!
coverage: state coverage
SystemVerilog for Verification

## Slide 184: Coverage Report
SystemVerilog for Verification

## Slide 185: Let’s Synthesize!
Coverage is at an acceptable level?
  Sign off on RTL
Design is synthesized unto low level primitives. Now what?

## Slide 186: Logical Equivalence Segment
Students will learn the common faults that can be introduced in the synthesis stage.
Students will learn of common logical equivalence tools and the concepts behind them.

## Slide 187: Synthesis Mismatch
Mismatches between RTL and Synthesized Netlist can occur
Remember HDL stands for Hardware “Description” Language.
Synthesis tool can misinterpret what was described.

## Slide 188: Practices that lead to Mismatches
Incomplete sensitivity list
  Netlist will trigger on any change regardless of sensitivity list
Complete sensitivity list with mis-ordered assignments
  Assignments in blocks execute sequentially in RTL sim.
  Synthesis will order assignment correctly based on dependencies.

## Slide 189: Practices that lead to Mismatches
Functions:
  no synthesis tool warnings when function code simulates latch behavior
Improper initialization
  Fpga designers can initialize variables… ASICs can’t.
Timing Delays
  Placing delays on the left side of always block assignments does not accurately model either RTL or behavioral models.

## Slide 190: How do we verify Equivalence?
Verify Netlist through simulation
  Use same verification code on netlist.
Most vendors provide simulation libraries for their primitives.
  Can be difficult to work with
  Google “glbl.v error” later.

## Slide 191: How do we verify Equivalence?
Can instantiate both RTL and Netlist in design.
  Verify that given the same inputs they produce same outputs.
Problem?
  Many synthesis tools will reorder signals to meet timing.

## Slide 192: Equivalence checking
It is necessary to match the variable names of the designs under comparison!
We implement canonical forms ...
... or look for an input vector that would distinguish the output responses of two designs. SAT methods. Similar to test pattern generation.

## Slide 193: Equivalence checking
Comparison of pre- and post-scan schematics
Comparison of RTL versus transistor layout
Verification of minor changes in the design

## Slide 194: Logic Equivalence check
Tool validates the design by injecting random vectors
Conformal from Cadence and Formality from Synopsys
Opensource: Yosys

## Slide 195: Logic Equivalence check: Process
Specify Blackbox parts of design.
Read in libraries and designs
Specify design constraints
Specify modeling directives
Switch to LEC mode
  Mapping process
  Compare process

## Slide 196: LEC: Specification of blackbox
Non-essential/Negligible design parts broken down into blocks
  i.e analog blocks, memories, and digital blocks.
  blocks are treated as blackbox when running LEC.
  IPs can be included as blackbox.
makes sure only the I/O ports are read and not the entire design.
cut the runtime by a huge amount and will be of great assistance when we are running LEC on large designs

## Slide 197: LEC: Read RTL and Libraries
Read Verilog and VHDL file
Read in standard simulation libraries
built-in Hardware Descriptive Language (HDL) rule check searches for lint errors and warnings.

## Slide 198: LEC Specification of design constraints
DFT insertion can create multiple functional modes for design
adding constraints to the design to ensure it is in common functional mode
I.E: Tie scan_enable to zero

## Slide 199: LEC Specification of modeling directives
Synthesis can output different netlist optimizations
  Power optimized, Area optimized, Effort optimized
Clock gating logic in golden design would be converted to latch-based clock gating.
Need to add modeling directives to match both designs.

## Slide 200: LEC Mapping process
maps key points such as
  primary inputs (PI), primary outputs (PO), DFFs, D-latches, blackboxes, Z-gates, and cut gates
First will use name-based mapping
Followed by function-based mapping
Name-based mapping takes less runtime than function-based mapping
  tools tries to map key points with name-based mapping before switching to function based mapping.

## Slide 201: LEC Compare process
Comparison done only on mapped key points.
  important that all key points should be mapped
Will try to prove equivalency by passing all combinations of inputs to the logic cone and checks the output behavior.
After running, key points will be categorized as equivalent, inverted equivalent, non-equivalent, and abort points.
If all the compare points come out as equivalent, then we can confidently assert that the golden and revised design are matching.

## Slide 202: Formal Verification Segment
Students will learn the basics of formal verification.
Students will be able to apply bounded models to logic designs.
An Introduction to Formal Methods

## Slide 203: Formal Verification
Problem with test benches?
  Only examines a known good branch
  Cannot check for every out of bounds conditions
  Demonstrate design works
    Through a normal working path – or a limited number of extraneous paths
  Never rigorous enough to check everything
  Not uniform in rigor
I.E
  For a FIFO
    Only read when you know it’s not empty
An Introduction to Formal Methods

## Slide 204: Simulation-based vs formal

## Slide 205: Model-checking
The goal is to find an input assignment violating the assumed property.
If such an assignment (counter-example!) exists then we can simulate it to obtain signal waveforms for debugging.
If there exists no counter-example then we have proven that the implementation matches the property.

## Slide 206: Model-checking
Problems:
How do you extract only this portion of the design that is related to the property to be checked. Currently done manually...
Selection of the properties to be checked is tricky...
Bugs may occur in the implementation, in properties or in configuration (i.e. environment).
Roughly 70 % of total effort for setting up the configuration.

## Slide 207: Model-checking
Theorem provers
Not very automated but...
handle larger designs, require less memory.
Use higher order logic.
  Thus, can check more complex properties.

## Slide 208: Formal verification Flow

## Slide 209: Basic Premise
Two separate and distinct fashions
  First method calculates the answer
  Second method proved it was right
Formal is similar
  Design is the first method
  Formal properties are the second
An Introduction to Formal Methods
Example: Division
  Does it?
  Let’s check: — Yes!

## Slide 210: Basic Premise
An Introduction to Formal Methods
Example: Division
Does it?
Let’s check:
— Yes!

## Slide 211: Basic Premise
Formal is similar
  Design is the first method
  Formal properties are the second
An Introduction to Formal Methods

## Slide 212: Basics
Assert
  An assert ( X ) statement indicates that X must be true, or the design will fail to prove
Assume
  An assume ( X ) statement will limit the state space that the formal verification engine examines.
An Introduction to Formal Methods

## Slide 213: Assert/assume forms
An Introduction to Formal Methods

## Slide 214: General Rule
An Introduction to Formal Methods

## Slide 215: Assert
Assertions define the illegal state space.
Additional assertions will increase the size of the illegal state space.
An Introduction to Formal Methods

## Slide 216: Assume
Assumptions limit the universe of all possibilities
Additional assumptions will decrease the size of the total state space
  Caution: careful not to make assumptions that are impossible
  I.E., assume a 4-bit signal is greater than 30
An Introduction to Formal Methods

## Slide 217: Bounded Model Checking
For bounded model checking:
  Start at the initial state
  Examine all possible states for N clocks
  Try to find a way to make an assert (); fail
  If it’s not possible in N clocks, then pass
An Introduction to Formal Methods

## Slide 218: No Solution
Problem: initial assume(!initial_state); Model fails, no line number given.
Problem: assume(!reachable_state); Model fails, no line number given.
An Introduction to Formal Methods

## Slide 219: Assertions vs Assumptions
Suggestion,
  Any SystemVerilog properties that constraints the input state-space of our DUT are assumptions.
  Properties that checks the validity of output signals are assertions.

## Slide 220: BMC UART
Consider relationship between inputs and outputs
For this DUT we need to cover forward progress, rdy handshaking, tx_busy propagation.
Uart Protocol??
  Testbench/BFM will confirm protocol
  Caveat, should be robust enough to find errors in protocol/ protocol violations.

## Slide 221: BMC Example
Extra points to suggests some more properties for UART

## Slide 223: BACKGROUND: K- Induction
Base case: prove for N = 0/1
Inductive step: Assume true for N, prove true for N + 1
For N = 1, the sum is or one
So, this is true (for x != 1).
For the inductive step, we’ll
  Assume true for N, then prove for N + 1
An Introduction to Formal Methods

## Slide 224: BACKGROUND: Proof
Assume true for N, prove for N + 1
Prove for N + 1
This proves the inductive case.
Hence this is true for all N (where N > 0 and x != 1 )
An Introduction to Formal Methods